## Slide 1
Number System
ESc201 : Introduction to Electronics
Vipul Arora
Dept. of Electrical Engineering
IIT Kanpur
Mar 20, 2023

## Slide 2: Writing Numbers
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
g
h
i
j
k
...
!
@
#
Better to write as 10, 11, 12
Fixed number of symbols + Compositionality
How many basic symbols?
Why 10, why not 2 or 5 or 8 or 16?

## Slide 3
Numbers
Every number system is associated with a base or radix (no. of symbols)
The decimal system has a base of 10 and uses symbols (0,1,2,3,4,5,6,7,8,9) to represent numbers
A positional notation is commonly used to express numbers

## Slide 4
Numbers
Every number system is associated with a base or radix (no. of symbols)
A positional notation is commonly used to express numbers

## Slide 5
Numbers
An octal number system has a base 8 and uses symbols (0,1,2,3,4,5,6,7)
What decimal number does it represent?

## Slide 6
A hexadecimal system has a base of 16
Number | Symbol
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 8
9 | 9
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F
How do we convert it into decimal number?
Numbers

## Slide 7
A Binary system has a base 2 and uses only two symbols 0, 1 to represent all the numbers
Which decimal number does this correspond to ?
1 1 0 1 . 1 0 0 1
23
22
21
20
2-1
2-3
2-2
2-4
20 | 1
21 | 2
22 | 4
23 | 8
24 | 16
25 | 32
26 | 64
27 | 128
28 | 256
29 | 512
210 | 1024(K)
220 | 1048576(M)
2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625
13. 5625

## Slide 8
1 1 0 0 1 = ?
Developing Fluency with Binary Numbers
25
1100001 = ?
64+32+1=97
0.101 = ?
0.5+0.125=0.625
11.001 = ?
3+0.125=3.125

## Slide 9
Converting decimal to binary number
Convert 45 to binary number
Finding coefficients: divide both sides by 2

## Slide 10
Divide both sides by 2

## Slide 11
Notes: Successive division

## Slide 12
Converting decimal to binary number
Method of successive division by 2
45
22
1
remainder
11
0
5
1
2
1
1
0
0
1
45 = 1 0 1 1 0 1
44 = 1 0 1 1 0 0
Notes: Can I talk in terms of mod?

## Slide 13
Convert (153)10 to octal number system
Divide both sides by 8
153
19
1
remainder
2
3
0
2
153 = (231)8

## Slide 14
Converting decimal to binary number
Convert (0.35)10 to binary number
How do we find the b-1 b-2 …coefficients?
Multiply both sides by 2

## Slide 15
Multiply both sides by 2
Note that ½+1/4+1/8+……1

## Slide 16
0 .
0 .
25
125
5
1.
0
0.125 = (.001)2
x2
x2
0 .
x2
0.125 = ?
0.8125 = ?
0 .
1 .
625
8125
25
0.
5
x2
x2
1 .
x2
1.
0
x2
0.8125 = (.1101)2
Converting decimal to binary number

## Slide 17
Binary numbers
1011000111
Binary digit = bit
Least significant bit or LSB
Most significant bit or MSB
This is a 10 bit number
decimal | 2bit | 3bit | 4bit | 5bit
0 | 00 | 000 | 0000 | 00000
1 | 01 | 001 | 0001 | 00001
2 | 10 | 010 | 0010 | 00010
3 | 11 | 011 | 0011 | 00011
4 |  | 100 | 0100 | 00100
5 |  | 101 | 0101 | 00101
6 |  | 110 | 0110 | 00110
7 |  | 111 | 0111 | 00111
8 |  |  | 1000 | 01000
9 |  |  | 1001 | 01001
10 |  |  | 1010 | 01010
11 |  |  | 1011 | 01011
12 |  |  | 1100 | 01100
13 |  |  | 1101 | 01101
14 |  |  | 1110 | 01110
15 |  |  | 1111 | 01111
N-bit binary number can represent numbers from 0 to 2N -1

## Slide 18
Converting Binary to Hex and Hex to Binary
Number | Symbol
0(0000) | 0
1(0001) | 1
2(0010) | 2
3(0011) | 3
4(0100) | 4
5(0101) | 5
6(0110) | 6
7(0111) | 7
8(1000) | 8
9(1001) | 9
10(1010) | A
11(1011) | B
12(1100) | C
13(1101) | D
14(1110) | E
15(1111) | F
h1
h0
Notes: Add a + in h0 bracket

## Slide 19
Binary Addition/Subtraction
Notes: These examples rae only for addition. Subtraction is slightly complicated. Therefore first define complements.

## Slide 20
Complement of a number
Decimal system:
9’s complement
10’s complement
9’s complement of n-digit number x is 10n -1 -x
10’s complement of n-digit number x is 10n -x
9’s complement of 85 ?

## Slide 21
Complement of a binary number
Binary system:
1’s complement
2’s complement
1’s complement of n-bit number x is 2n -1 -x
2’s complement of n-bit number x is 2n -x
1’s complement of 1011 ?
1’s complement is simply obtained by flipping a bit (changing 1 to 0 and 0 to 1)

## Slide 22
Leave all least significant 0’s as they are, leave first 1 unchanged and then flip all subsequent bits

## Slide 23: Arithmetic Including Negative Numbers
A digital system has finite number of bits
For n bits available, 2n unique numbers can be represented
There is need to be able to represent negative number
We would like a link between negative and positive number
  Likely to make the math easy
We would like to have a unique representation of zero
We would like to do arithmetic (addition and subtraction)
Positive and negative numbers are generated during arithmetic operations
Finite size available to represent numbers will bring in constraints
But we want to optimise as much as possible within the constraints

## Slide 24: Representing Positive and Negative Numbers
Extra bit needed to carry sign information
“MSB” is often the sign bit
Unique zero
representation
2n-1 – 1
positive nos.
2n-1
negative nos.
magnitude
magnitude
magnitude
magnitude
2’s comp. of
0 and -8 are themselves
magnitude
magnitude
Sign bit = 0 represents non-negative nos.
Sign bit = 1 represents negative numbers
One option

## Slide 25: Summary
Represent –ve numbers as 2’s complement, i.e.,
  If the MSB is 0, take the number as positive
  If the MSB is 1, take the 2’s complement to get the magnitude, and the sign is negative.
Advantage of 2’s complement:

## Slide 26: Arithmetic with 2’s Complement
for LSB
for MSB

## Slide 27
Example
2’s complement is 0011 = 3
2’s complement is 0111 = 7
2’s comp.
of +2
2’s comp.
of +5
2’s comp.
of +2
2’s comp.
of +5
Adding or subtracting numbers with addition operation alone